## Slide 1
🤖
Face Learning &
Recognition Behavior
NAO / Pepper Robot · Choregraphe + NAOqi
An end-to-end behavior that learns a face and greets recognized people by name.
Text Edit
→
Learn Face
→
Face Reco.
→
Say Hello

## Slide 2
Overall Behavior Flow
onStart
Behavior
begins
→
Text Edit
"antonio"
→
Learn Face
5s + camera
learning
→
Face Reco.
Monitor
camera
↙
↘
✅ Known Face
"Hello antonio!"
❌ Unknown Face
"I don't know you"
LearnFace result:
🟢 Eyes GREEN = success
🔴 Eyes RED = failure
Key Concepts
ALFaceDetection — NAOqi module that handles all face learning & recognition · ALMemory FaceDetected — event fired every time camera sees a face · ALTextToSpeech — robot speech output

## Slide 3
Stage 1
Text Edit Box
The starting point — assigns a name to the face being learned
def onInput_onStart(self):
self.onStopped("antonio")
🚀
Triggered when the behavior starts via onStart signal
📛
Sends name "antonio" immediately to its output
🔗
Passes name forward to the LearnFace box input
💡
Easily changed to any name — just edit the Text Edit plugin value
Think of this box as telling the robot: "The person you're about to see is called antonio"

## Slide 4
Stage 2
LearnFace Sub-Behavior
5 internal boxes work together to safely learn a face
1
Only Once
Ensures learning
triggers just once
→
2
Wait 5s
Person positions
in front of camera
→
3
Eyes LEDs 🔵
Blue eyes = robot
is getting ready
→
4
WaitToSend
Syncs name + timer
before learning
→
5
learnFace()
ALFaceDetection
stores the face
Result:
🟢 Eyes GREEN — Face stored in database
🔴 Eyes RED — No face detected / failed
⭐ Core — learnFace() call
result = self.faceDetectionModule.learnFace(p) # p = "antonio"
if result: self.onSuccess() # Eyes GREEN
else: self.onFailure() # Eyes RED

## Slide 5
Stage 3
Face Reco. Box
How It Works
👁️
Subscribes to ALMemory FaceDetected event
📊
Confidence threshold set to 0.8 (80%)
🔍
Parses nested face data array from camera
✅
Known face → fires onRecognizedFace(name)
❓
Unknown face → fires onDetectWithoutReco
Recognition Logic
# Set 80% confidence threshold
self.faceProxy
.setRecognitionConfidenceThreshold(0.8)
# Check if faces present
if len(p) > 0 and len(p[1]) > 0:
result = p[1][len(p[1])-1]
if result[0] == 4:
# Detected but NOT recognized
self.onDetectWithoutReco()
elif result[0] in [2, 3]:
# RECOGNIZED — send name
for name in result[1]:
self.onRecognizedFace(name)

## Slide 6
Stage 4
Say Boxes — Robot Speech
Two different responses depending on recognition outcome
✅ Say Box — Known Face
def onInput_onStart(self, p):
sentence = "Hello " + str(p) +
" I recognize you!"
self.tts.say(sentence)
self.onStopped()
p = name string from Face Reco. output
Builds:
"Hello antonio I recognize you!"
💬 Uses ALTextToSpeech to speak aloud
❌ Say (1) Box — Unknown Face
def onInput_onStart(self):
sentence = "I see you, but I do
not know your name yet.
Please teach me!"
self.tts.say(sentence)
self.onStopped()
No parameter needed — triggered when face
detected but NOT in database
💬 Politely invites the person to be learned

## Slide 7
Complete Flow Summary
1
🚀 Behavior Starts
onStart signal triggers the whole chain
2
📝 TextEdit sends "antonio"
Name passed to LearnFace input
3
🔒 Only Once — gates the signal
Prevents repeated learning attempts
4
⏱️ Wait 5 seconds (Eyes = BLUE 🔵)
Person positions their face in front of camera
5
🔗 WaitToSend synchronizes
Name + timer signal both arrived → proceed
6
🧠 learnFace("antonio") called
ALFaceDetection captures and stores the face
7
💡 Eyes GREEN ✅ or RED ❌
Visual feedback of success or failure
8
👁️ Face Reco. monitors camera
ALMemory FaceDetected event fires continuously
9
🔊 Say the result
"Hello antonio!" or "I don't know you yet"

## Slide 8
🤖
Thank You
Face Learning & Recognition on NAO/Pepper
✦ ALFaceDetection handles all face ML internally
✦ WaitToSend synchronizes timing perfectly
✦ 80% confidence threshold avoids false positives
✦ Fully tested and working on real NAO/Pepper